## Slide 1: Safety in Open Source Radioisotope Laboratories
This presentation will introduce you to the theory of radioisotopes and the procedures used in their safe handling.

## Slide 2: Radiation
Definition: Radiation is the energy in the form of particles or waves
Two Types of Radiation
  Ionizing: removes electrons from atoms
    Particulate (alphas and betas)
    Waves (gamma and X-rays)
  Non-ionizing (electromagnetic): can't remove electrons from atoms
    infrared, visible, microwaves, radar, radio waves, lasers

## Slide 3: Nomenclature for Elements
"X" = Element Symbol
"Z" = # Protons
  Each element has a unique "Z”
"N” = # Neutrons
Atomic Mass # = "A“
"A" = Z + N = # Protons + # Neutrons
Isotope: same Z, different N, thus different A
Radioisotope: An unstable isotope

## Slide 4: Phosphorous
15 Protons
P-31
    16 Neutrons and stable
P-32
    17 Neutrons and unstable
P
31
15
P
32
15

## Slide 5: Decay Law & Half-Life
Half life: The time required to reduce the amount of a particular type of radioactive material by one-half
Example: 120 Ci of P-32 (t 1/2 = 14 days)
A(t) = A(0) * e
t
A(o) = Initial Activity
A(t) = Activity after time "t"
t = Decay time
λ = constant = 0.693 / t1/2
t 1/2 = half-life
0
20
40
60
80
100
120
140
0
14
28
42
56
70
84
98
Activity (curies)
Time (days)

## Slide 6: Gamma Radiation
Wave type of radiation - non- particulate
Photons that originate from the nucleus of unstable atoms
No mass and no charge
Travel many feet in air
Lead or steel used as shielding
Eg: I- 131

## Slide 7: Beta Particles
  Low mass (0.0005 amu)
  Low charge - can be positively or negatively charged (+/- 1)
  Travel 10 - 20 feet in air
  Stopped by a book
  Shield betas with low density materials such as lucite or plexiglass
  Shielding high energy betas like P-32 with lead can generate more radiation than it shields due to Bremsstrahlung X-rays

## Slide 8: Bremsstrahlung Radiation
Energy is lost by the incoming charged
particle through a radiative mechanism
Beta Particle
-
Bremsstrahlung Photon
+
+
Nucleus

## Slide 9: Alpha Particles
Alpha particles
  High mass (4 amu) = 2 protons + 2 neutrons – eg Ra-226
  High charge (+2)
  High linear energy transfer (cause great biological damage)
  Travel a few centimeters in air
  Stopped by a sheet of paper or protective layer of skin
  Not an external hazard
  Concern would be for ingestion or inhalation

## Slide 10
Examples of Nuclear Decay
Beta Plus Decay:
(neutron-deficient nuclides)
Alpha Decay:
(Heavy nuclides above
atomic number 82)
Beta Minus Decay:
(neutron-excess nuclides)

+
16
S
32
-
0
P
32
15

Ne
Na
22
22
11
+
10
0

Po
210
84
206
82
4
2
Pb
+
7

+
N
14
-
0
C
14
6

## Slide 11: Specific Radioactive Materials
Phosporous-32
  14.3 day half life
  High energy beta (1.710 MeV max)
  Shield with low Z material such as plastics
  Do not use lead shielding
  Wear safety glasses to shield eyes
  Ring badges are required for handling millicurie quantities
  GM survey meter required
  Avoid handling containers for extended periods

## Slide 12: Specific Radioactive Materials
Tritium (Hydrogen-3)
  12.3 year half life
  Very low energy beta (0.0186 MeV max)
  No shielding needed
  Surveys by wipe method counted on LSC
Carbon-14
  5730 year half life
  Low energy beta (0.156 MeV max)
  Shielding not needed
  Spot checks with GM are possible but contamination surveys using wipes are necessary

## Slide 13: Units of Measure
  Disintegrations per minute (dpm)
  Counts per minute (cpm)
  Disintegrations per second (dps)
  The SI unit for activity is the becquerel (Bq)
  1 Bq = 1 disintegration/second
  1 Curie (Ci) = 3.710 Bq or 37 GBq
    1 millicurie = 37 MBq
    1 microcurie = 37 kBq

## Slide 14: Units of Relative Biological Effectiveness (RBE)
The Sievert (SV) is the SI unit that takes into account the biological effects of the particular radiation emission based on the collision stopping power of the incident particle and is a measure of the potential biological injury of a particular type of radiation.
1 mSv= 100 mrems

## Slide 15: Sources of Ionizing Radiation (World)
Radiation Source | Annual Effective Dose
 | mSv | % of total
Natural |  | 
Cosmic | 0.30 | 8
g Rays from the Earth | 0.35 | 10
Internal Sources | 0.35 | 10
Radon | 1.00 | 29
Man-Made |  | 
Medical | 1.50 | 42
Weapons Testing | < 0.01 | < 0.03
Nuclear Power | < 0.01 | < 0.03
Total | 3.50 | 100

## Slide 16: ALARA
The goal of radiation protection is to keep radiation doses As Low As Reasonably Achievable
TRU is committed to keeping radiation exposures to all personnel ALARA (zero)
What is reasonable?
  Includes: -State and cost of technology
  -Cost vs. benefit
  -Societal & socioeconomic considerations

## Slide 17: Maternal Factors & Pregnancy
Statistically, a radiation exposure of 1 rem (0.01 mSV) poses much lower risks for a woman than smoking tobacco or drinking alcohol during pregnancy
Smoking
General
Babies weigh 5-9 oz. Less than average
< 1 pack/day
Infant Death
1 in 5
> 1 pack/day
Infant Death
1 in 3
Alcohol
2 drinks/day
Babies weigh 2-6 oz. Less than average
1 in 10
2-4 drinks/day
Fetal alcohol syndrome
1 in 3
> 4 drinks/day
Fetal alcohol syndrome
1 in 3 to 1 in 2
Radiation
1 rem
Childhood leukemia deaths before 12 years
1 in 3333
1 rem
Other childhood cancer deaths
1 in 3571

## Slide 18: Safety in Radioisotope Laboratories
It is important to remember and comply with these safety instructions.
Students not working according to these precautions may be asked to leave the lab.

## Slide 19: General Safety Precautions
No eating or drinking in the lab
Suitable footwear: no open toes or heels
Report all cuts, scrapes, burns or other injuries to the instructor
Keep fingers and objects away from your mouth and eyes
Notes: 19
Important to report injures so proper medical action is taken if required
Fingers pens etc near eyes may result is spread of biohazardous or chemical bench contaminants to eyes or mouth
Food is to be eaten in hallways

## Slide 20: General Radiation Safety Precautions
All students must wear a lab coat and gloves in the radioisotope lab
Always be aware of your surroundings and what you are doing
Use a face shield or screening when working with 32P

## Slide 21: General Radiation Safety Precautions
Time: minimize the time that you are in contact with radioactive material to reduce exposure
Distance: keep your distance. If you double the distance the exposure rate drops by factor of 4
Shielding:
  Lead, water, or concrete for gamma & X-ray. Thick plastic (lucite) for betas
Protective clothing: protects against contamination only - keeps radioactive material off skin and clothes

## Slide 22: General Safety Precautions
Disposal
  Ensure you have disposed of wastes in appropriate containers
It is important to wash hands thoroughly with a non-abrasive soap before leaving the lab or if you have spilled on your hands
Notes: Important to dispose of properly to avoid injury or spread of disease to others who cleanup the lab